## Slide 1: FCC Public Forum David Pollard – RAN Engineer November 6, 2017
Feb. 2012 - AT&T filed Petition for Rulemaking to modify FCC rule 22.913 to allow carriers to use PSD to calculate ERP for cellular base stations
June 2014 - AT&T successfully tests PSD with Miami Dade County Public Safety.
  2 B-Band UMTS carriers at 125W/MHz
  No interference or significant noise change
Sept. 2014-Dec. 2015 – FCC granted AT&T PSD waivers for SFL, VT, MO, & KS
  SFL - 125W/MHz
  VT, MO, & KS - 250W/MHz in non-rural;500W/MHz in rural
  ≥ 30 day advance notice to public safety within 113 km

## Slide 2
Mar. 2017 - FCC adopts R&O allowing all cellular carriers to use PSD to calculate ERP for base stations, bringing harmony with other spectrum bands, with conditions:
  400W/MHz in non-rural/800W/MHz in rural (no PFD)
  1000W/MHz in non-rural/2000W/MHz in rural. Until 05/12/24, 3000 µW/m²/MHz at 1.6 meters AGL over at least 98% of a 1 km radius
  ≥ 30 day advance notice to public safety within 113 km
  AT&T & VZ each committed to:
    test with public safety in 6 diverse markets & report results (advance notice)
    roll-out PSD in a cluster of sites in 10 markets before full market roll-out after 60-days if no unmitigated unacceptable interference (advance notice)
    AT&T testing will mimic Miami Dade County testing (ON/OFF): PSE transmission successful, using various PSE equipment, multiple sites and distances from sites, monitor BER, C/I and interference.