## Slide 1: Working Group 2: Comprehensive Re-imagining of Emergency Alerting
December 13th, 2018
Dr. Farrokh Khatibi, Chair (Qualcomm Technologies, Inc.)

## Slide 2: WG2 Objectives
Working Group Description:
The Commission directs CSRIC to conduct a comprehensive evaluation of emergency alerting and emerging technologies (such as the ATSC 3.0 broadcast standard and 5G) that may result in new alerting capabilities. As part of this evaluation, this Working Group would develop recommendations for CSRIC’s consideration on ways to streamline, simplify (by reducing burdens on licensees), and modernize existing systems, including the Emergency Alert System (EAS). This Working Group will review the processes and requirements for the EAS and related systems, and develop recommendations for CSRIC’s consideration regarding any necessary technical protocols and processes to improve the functionality of EAS, including coordination of messages formatted in both the CAP and EAS protocol, as well as the reliability of emergency alerts by strengthening the authentication and integrity of these systems, including the EAS. As part of this overall evaluation, this Working Group develop recommendations on any technical solutions to support authentication of alerts through digital signatures for both the Internet-based IPAWS and the broadcast-based legacy “daisy chain” to ensure that the alert retransmitted by an EAS Participant was generated by an authorized alert originator and has not been modified since its generation. This Working Group also will examine whether any amendments or changes to existing technical protocols (including the Commission’s rules or existing technical standards) are necessary to ensure the alert is only retransmitted during its valid period (e.g., during its current year, day, and time) and, if so, provide corresponding recommendations.
Deliverables:
  Report on Re-imagining Alerting – June 2018 (completed).
  Report on Security Aspects of EAS – December 2018.
  Report on Re-Imagining Alerting – Amended – December 2018.

## Slide 3: WG2 Members
3
* Also a CSRIC member
Name | Company
Farrokh Khatibi* - Chair | Qualcomm Technologies, Inc.
Brian Daly | AT&T Access Architecture & Devices Wireless Network Architecture & Design
Charlotte Field | Charter Communications
Claude Stout | TDI -Telecommunications for the Deaf and Hard of Hearing
Dana Golub | Public Broadcasting Service Warning, Alert, Response Network project “WARN”
Denis Gusty | Department of Homeland Security
Edward Czarnecki* | Monroe Electronics Inc.
Francisco Sanchez* | Harris County Office of Homeland Security & Emergency Management
Gary Smith* | Cherry Creek Radio
Glenn Edwards | Bayou City Broadcasting
Harold Price | Sage Alerting Systems
Kelly Williams | National Association of Broadcasters
Kevin Gage* | One Media LLC.
Mark D. Annas | City of Riverside - Office of Emergency Management
Mark Paese | U.S. Department of Commerce National Oceanic and Atmospheric Administration (NOAA) National Environmental Satellite & Information Service
Robert Gessner* | American Cable Association
Roger Stone* | Federal Emergency Management Agency DHS-FEMA
Susan Miller* | Alliance for Telecom Industry Solutions (ATIS)
William A. Check | NCTA – The Internet & Television Association
Steven Carpenter | FCC
Austin Randazzo | FCC

## Slide 4: WG2 Alternate Members*
Name | Company
Andy Scott | NCTA – The Internet & Television Association
Craig Saari | Charter Communications
Mark Lucero | Federal Emergency Management Agency DHS-FEMA
Mary Lovejoy | American Cable Association
Mike Gerber | National Oceanic and Atmospheric Administration (NOAA) U.S. Department of Commerce National Environmental Satellite & Information Service
Steve Barclay | Alliance for Telecom Industry Solutions (ATIS)
* Although the alternates are not a member of the Working Group and may not vote, they provided valuable input towards the completion of this report that should be acknowledged.

## Slide 5: Background
It is critical to send the relevant emergency information in a timely fashion to the targeted individuals in an affected area in a secured manner.
Authentication of EAS through digital signatures for the Internet-based IPAWS using CAP in all messages received by EAS Participants is being investigated, to ensure that the alert retransmitted by an EAS Participant was generated by an authorized Alert Originator (AO) and has not been modified since it's generation. This requirement should be expanded to all CAP messages received and retransmitted by an EAS Participant.
Specific requests from FCC for Recommendations in “Amendment of Part 11 of the Commission's Rules Regarding the Emergency Alert System; Wireless Emergency Alerts (FCC)”

## Slide 6: Types of False EAS
From Authorized Sources
  Generated by a person or persons (e.g., Hawaii)
  Automated cross-platform software
    Automated software sends a message in error (Test Tsunami warning from a non-EAS source incorrectly interpreted as live event and then sent via EAS)
  Misconfigured Test
No changes to the EAS protocol will help in these cases.

## Slide 7: Types of False EAS
Unauthorized Access to authorized location
  Unauthorized person sends a message from an agency that the agency did not authorize (Zombie)
No changes to the EAS protocol will help in these cases. Identified mitigations include maintaining sensitive equipment behind firewall protection, changing default passwords, maintaining a strong password policy on the part of end users (EAS Participants).

## Slide 8: Types of False EAS
Replay
  Valid alert resent outside of its valid time period that fits inside the JJJHHMM of the original message – no intentional cases known.
  Valid alert resent outside of its valid time period that does not fit inside the JJJHHMM of the original message (Bobby Bones, replay in “best of” reruns)
The intent of mitigations for replay events is to keep other EAS participants from relaying the alert. This replay alert still appears on the source, where it can cause audience confusion.

## Slide 9: Types of False EAS
Audience confusion
  Audio presented to the audience that “sounds like” an alert, but isn’t. Affects listeners, but is not relayed. (Advertising intentionally intended to sound like an alert)
No changes to the EAS protocol will help in these cases.

## Slide 10: Types of False EAS
Alert from an unauthorized source
  CAP
    Spoofed CAP messages that somehow make their way through the FEMA IPAWS OPEN system, or are presented to an EAS Participant from a system pretending to be the IPAWS system, or from legitimate, third-party relayer of IPAWS CAP messages.
      The group conducted analysis of the CAP authentication on its validity, the source of digital certificate, and the security of the multimedia content.
  EAS
    Use of some type of digital signature as a remedy to a secure EAS.
      The group conducted analysis of the EAS digital signature including advantages, costs, risks, new limitations, and risk mitigation.

## Slide 11: Broadcast EAS Authentication
Requirement for internet access to verify signatures
Background on EAS Headers and SAME Protocol
Inserting a Digital Signature into the EAS Header
Additional concepts for EAS message security
  Concept 1: EAS security can be enhanced through inclusion of a YY or YYYY year code.
  Concept 2: EAS security can be potentially enhanced through a repurposing of the station ID element (LLLLLLLL) in the EAS header.
Alternative methods of inserting additional data into the EAS header

## Slide 12: Recommendations
All CAP messages that are intended for transmission as EAS messages must have a valid digital signature.
The Commission should evaluate whether digitally signed CAP messages processed by EAS Participants should only rely on digital certificates issued by FEMA IPAWS, relying on the on the Federal PKI and chain of trust
  Compared to allowing alternative (State, Territorial, Tribal, and Local) digital certificate sources.

## Slide 13: Recommendations
Additional investigation be conducted into the use of digital signatures as a solution to EAS security, comparing risks vs cost.
Additional investigation be conducted into technical or system impacts – if any - to allowing the usage of embedded audio files in CAP alert messages.

## Slide 14: Recommendations
In general, the Commission should engage with its Federal and Industry partners to evaluate the technical feasibility and system impacts of solutions discussed by the working group.

## Slide 15: Personal Note
I would like to thank all the WG2 members, alternates, and participating SMEs without whom the work could not have completed.
I would also like to thank ATIS for providing meeting tools that facilitated the work progress.
It was a privilege chairing CSRIC VI Working Group 2.