## Slide 1: Fourth Meeting of THE COMMUNICATIONS SECURITY, RELIABILITY, AND INTEROPERABILITY COUNCIL VIII
JUNE 15, 2022

## Slide 2: Open Meeting & Welcome Suzon Cameron, DFO

## Slide 3: Opening Remarks
CSRIC VIII Co-chair
Nasrin Rezai, Verizon

## Slide 4: Presentation
WG1: Co-chairs
Brian Daly, AT&T
Travis Russell, Oracle
WG1: 5G Signaling Protocols Security

## Slide 5: Working Group 1: 5G Signaling Protocols Security
June 2022
Co-chairs:
Brian Daly, AT&T
Travis Russell, Oracle Communications
FCC Liaison: Ahmed Lahjouji

## Slide 6: Working Group 1: Background
The Chairwoman of the FCC directs CSRIC VIII to examine and address security vulnerabilities associated with the newly adopted 5G signaling protocol, Hypertext Transfer Protocol Version 2 (HTTP/2), which, like the SS7 and Diameter signaling protocols considered in earlier CSRICs, is vulnerable to attacks. Researchers have discovered security issues related to the HTTP/2 protocol which could place millions of websites at risk of attack. CSRIC VIII will confirm these vulnerabilities and identify others, assess their potential for harm, and recommend safeguards to harden 5G networks and protect critical business and consumer data from these and other cyber threats. CSRIC VIII will also provide recommendations on how to remediate the risks associated with HTTP/2 and prevent them from carrying over to HTTP/3, the next release of the protocol.

## Slide 7: Working Group 1: Objectives
The FCC has learned of four main vulnerabilities and attack vectors related to HTTP/2:
  (1) slow read attacks, which call on a malicious client to read responses very slowly;
  (2) HPACK Bombs, which are malicious archive files designed to crash the program or system reading them and often disable antivirus software;
  (3) Dependency Cycle attacks, which exploit a new flow mechanism designed to optimize networks to instead create an infinite loop which cannot be escaped; and
  (4) Stream Multiplexing Abuse, which uses security flaws in stream multiplexing functionality to crash servers, resulting in a denial of service to legitimate users.
We will research these as well as other vulnerabilities and attack vectors identified by industry through industry SMEs and WG member expertise.

## Slide 8
Working Group 1: Members
  *Also a CSRIC VIII Member
  Colin B. Andrews,* Telecommunications Industry Association
  Michael Bergman,* Consumer Technology Association
  Matt Carothers, Cox Communications
  Martin Goldberg,* National Security Agency
  Angel V. Gomez, Verizon Communications
  Stephen Hayes,* Ericsson
  Jithin Jagannath, ANDRO Computational Solutions
  Antwane Johnson,* FEMA
  Xiaoyang Lee, CISA
  John Marinho, CTIA
  Martin McGrath, Nokia
  Maureen C. Mclaughlin,* Satellite Industry Association
  Danny McPherson,* Verisign, Inc.
  Derek Peterson,* Wireless Broadband Alliance
  Mitch Rappard, Palo Alto Networks
  Mike Recchione, ATIS
  Greg Schumacher, T-Mobile
  Anish Sharma, Mavenir
  Christopher Wendt, Somos, Inc.
Co-chairs: Brian Daly,* AT&T
Travis Russell,* Oracle
FCC Liaison: Ahmed Lahjouji

## Slide 9
Working Group 1: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Adam Barron, Verizon Communications
  Martin C. Dolly, AT&T, Inc.
  Carroll Gray-Preston, ATIS
  J. David Grossman, CTA
  Brandon Hinton, Satellite Industry Association
  Bradley Jackson, Verizon Communication
  Navin Jaffer, CISA
  Yong Kim, Verisign, Inc.
  Mark Lucero, FEMA
  John Mattson, Ericsson
  Tom McGarry, Telecommunications Industry Association

## Slide 10: Working Group 1: Deliverables/Schedule
WG virtual meetings (initially biweekly) are underway
  Research/examine security vulnerabilities and attack vectors
Report on Security Vulnerabilities in HTTP/2, September 2022
Report on Best Practices to Mitigate Vulnerabilities in HTTP/2 and HTTP/3, June 2023

## Slide 11: Working Group 1: Status of Work
The group continues research into other possible HTTP/2 protocol vulnerabilities
  Most of the vulnerabilities are specific to Internet applications and not 5G
  The team agrees that an HTTP/2 vulnerability in the open Internet may not be a vulnerability in a 5G context because of the closed nature of the network
Lots of discussion around other product specific vulnerabilities that show up in searches
  These are really “bugs” in products that are used for processing HTTP/2 transactions
  The team agrees that this is outside the scope of our charter and would not serve any value to this report

## Slide 12: Working Group 1: Status of Work
Bi-Weekly meetings continue, with a few exceptions
  We have had to cancel two meetings due to conflicts, but this does not impact the overall schedule
  The team is now focused on the report and making good progress on the document – there should not be any issue with deadlines

## Slide 13: Discussion
WG1: Co-chairs
Brian Daly, AT&T,
Travis Russell, Oracle
WG1: 5G Signaling Protocols Security

## Slide 14: Presentation
WG2: Co-chairs
Mike Barnes, Mavenir
George Woodward, RWA
WG2: Promoting Security, Reliability, and Interoperability of ORAN Equipment

## Slide 15: Working Group 2: Promoting Security, Reliability, and Interoperability of Open Radio Access Network Equipment
June 15, 2022
Co-chairs:
Mike Barnes, Mavenir
George Woodward, RWA
FCC Liaison: Zenji Nakazawa

## Slide 16: Working Group 2: Background
The Chairwoman of the FCC directs CSRIC VIII to provide recommendations to advance security, reliability, and interoperability of Open Radio Access Network (ORAN) equipment in the United States and what new efforts can be undertaken to support secure and interoperable ORAN design and deployment.
The Radio Access Network (RAN) is the final link between the network and the phone. It includes the antennae on towers, buildings, and in stadiums, plus the base stations. When a consumer makes a call or connects to a remote server, the antenna transmits and receives signals to and from the consumer’s mobile phone or other handheld device. The signal is then digitalized in the RAN base station and connected into the network.
The introduction of ORAN enables mobile network operators to use equipment from multiple vendors and still ensure interoperability.

## Slide 17: Working Group 2: Objectives
CSRIC has previously considered security risks in emerging 5G networks.
CSRIC VIII will build on this work and expand it as one part of its exploration of the development and deployment challenges facing ORAN technology, including the extent ORAN technology may increase the threat attack surface and how best to mitigate such security challenges.
Further, CSRIC VIII will consider how the FCC can support the goals of developing and deploying secure, open and interoperable networks when the FCC participates in standards-setting bodies like 3GPP and the Alliance for Telecommunications Industry Solutions.

## Slide 18
Working Group 2: Members
  *Also a CSRIC VIII Member
Rob Alderfer,* Charter Communications
Robert Dew, CISA
Marla Dowell,* NIST
Andrew L. Drozd,* ANDRO Computational Solutions
Russ Gyurek, Cisco Systems, Inc.
Javed Khan,* Altiostar Networks
Michael Loushine, AT&T, Inc.
Jennifer Manner,* Hughes Communications
Martin McGrath, Nokia
Jack Nasielski, Qualcomm Technologies, Inc.
Scott Poretsky, Ericsson
Vishwanath Ramamurthi, Verizon Communications
Stefan Saroiu, Microsoft Corporation
Tom Sawanobori,* CTIA
Tim Schram,* NARUC
Nick Solano, Qcommunications, LLC
Eric Tamarkin, Samsung Electronics America
Jean Trakinat, T-Mobile
Claire Vishik,* Intel
Henry Young,* BSA | The Software Alliance
Tim May,* NTIA
FCC Liaison: Zenji Nakazawa
Co-chairs: Mike Barnes,* Mavenir
George Woodward,* RWA

## Slide 19
Working Group 2: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Reza Arefi, Intel
  Brian Daly, AT&T
  Arvind Kumar, Mavenir
  Heidi Obermeyer, BSA | The Software Alliance
  Anand Palanigounder, Qualcomm
  Sanil Rama Chandran, Samsung
  James B. Ramsay, NARUC
  Imtiaz Shaikh, Ericsson
  Lakhbir Singh, Charter Communications
  Matthew Sneed, Hughes Communications
  Ryan Stokes, Rural Wireless Association
  Melanie Tiano, CTIA
  Lap Tse, Verizon Communications
  Timothy O. Woods, ANDRO Computational Solutions

## Slide 20: Working Group 2: Deliverables/Schedule
14-June 2022 - First Draft complete
13-Sept-2022 – Begin Final Review
15-Nov-2022 - Paper and Slides complete, submitted FCC
December 2022: Report on Challenges to the Development of ORAN Technology and Recommendations on How to Overcome Them

## Slide 21: Next Working Group 2 Meeting Agenda
Review First Draft
20-21 July 2022 - Face to Face and joint meeting with WG3 (Wash D.C)

## Slide 22: Discussion
WG2: Co-chairs
Mike Barnes, Mavenir
George Woodward, RWA
WG2: Promoting Security, Reliability, and Interoperability of ORAN Equipment

## Slide 23: Presentation
WG3: Co-chairs
Micaela Giuhat, Microsoft
John Roese, Dell
WG3: Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks
Presenter – Jeff Goldthorp, FCC

## Slide 24: Working Group 3: Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks
Co-chairs:
Micaela Giuhat, Microsoft
John Roese, Dell
FCC Liaison: Jeff Goldthorp

## Slide 25: Working Group 3: Background
CSRIC VIII will develop recommendations for how vendor-agnostic, horizontal stack solutions for 5G can be promoted to foster a diverse, competitive, and more secure 5G environment despite the wider attack surface presented. These recommendations should address ways to provide opportunities for smaller vendors that cannot yet manufacture all parts of a vertically integrated, traditional 5G stack.
In its first report on this subject, CSRIC VIII’s will include recommendations on ways in which funds can be made available to promote virtualized environments that result in improved 5G security and reliability; recommendations on ways to promote and overcome obstacles to the availability of virtualized central units (vCU) and virtualized distributed units (vDU) to increase 5G vendor diversity; best practices for reliability and interoperability that should be used by small businesses that contract or outsource as part of a multi-vendor 5G implementation; and other ways to promote a diverse 5G environment to improve 5G security and reliability. CSRIC VIII will also identify whether any additional work is needed from standards bodies such as 3GPP and ETSI on virtualization issues, such as addressing security risks relating to application programming interface (API) security.
Scope should include virtualization of the system which would include the core plus the CU, DO and possibly RU.
Virtualization in this context is more about the horizontal layering abstractions than the creation of open interfaces within a layer (E.g. eCPRI etc) However we should discuss if we have an opinion on “in layer open interfaces” being in scope.

## Slide 26: Working Group 3: Objectives
Review lessons learned from use of virtualization and higher vendor diversity in strengthening security, increasing competition, and creating a more secure supply chain
Gather input from researchers, technologists and thought-leaders and standard organizations on availability of solutions, and technical issues to be addressed
Perform an assessment of implementation best practices
  Perform comparison between virtualized and non-virtualized security vulnerabilities (theoretical and maybe practical?) in a 5G network
  Review results from test labs or real-life deployments around the world
  Identify issues to be addressed (e.g., API security)
Advise & recommend accordingly on how best to support a secure diverse vendor ecosystem:
  Funding
  Standards
  Integration best practices
  Ecosystem structures (who plays what roles in the open virtualized 5G ecosystem)
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability
Report on Recommendations on the Role of the FCC in Promoting the Availability of Standards for More Secure, Reliable 5G Environment Through the Use of Virtualization Technology

## Slide 27
Marla Dowell,* NIST
Andrew L. Drozd,* ANDRO Computational Solutions
Bob Everson, Cisco Systems, Inc.
Michael Gallagher, Verizon Communications
Martin Goldberg,* National Security Agency
Javed Khan,* Altiostar Networks
Douglas Knisely, Qualcomm Technologies, Inc.
Jennifer Manner,* Hughes Communications
Serge Manning, T-Mobile
Timothy May, NTIA
Martin McGrath, Nokia
William Mikucki,* Comtech Telecommunications Corp.
Keith O’Brien, Palo Alto Networks
Jitendra Patel, AT&T, Inc.
Leo Popokh, ATIS
Tom Sawanobori,* CTIA
Imtiaz Shaikh, Ericsson
Jane Shen, Mavenir
Paul Steinberg,* Motorola Solutions
Frank Suraci, CISA
Peter Tomczak,* FirstNet Authority
Claire Vishik,* Intel
Damien Whaley, Cox Communications
George Woodward, Rural Wireless Association
Working Group 3: Members
  FCC Liaison: Jeff Goldthorp *Also a CSRIC VIII Member
Co-chairs: Micaela Giuhat,* Microsoft
John Roese,* Dell
New workgroup member

## Slide 28
  Reza Arefi, Intel
  Kevin Green, FirstNet Authority
  Bryan Larish, Verizon Communications
  Doug Montgomery, NIST
  Vishwamitra, Nandlall, Dell Technologies
  Stere Preda, Ericsson
  Rowland Shaw, Dell Technologies
  Matthew Sneed, Hughes Communications
  Megan Stapleton, Comtech Telecommunications Corp.
  Darrell Stogner, Motorola Solutions
  Ryan Stokes, Rural Wireless Association
  Richard “Dick” Tenney, CISA
  Melanie Tiano, CTIA
  Timothy O. Woods, ANDRO Computational Solutions
Working Group 3: Alternates*
* Alternates are not a member of the Working Group and may not vote.
New alternate member

## Slide 29: Working Group 3: Milestones
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability - December 2022
Report on Recommendation on the Role of the FCC in Promoting the Availability of Standards for More Secure, Reliable 5G Environment Through the Use of Virtualization Technology - June 2023

## Slide 30: Working Group 3: Deliverables/Schedule
Scope and Methodology Agreement December 7th, 2021
Create list of SMEs and other industry bodies to be invited January 2022
Finish gathering of information June 2022
Create paper outline/sections July 2022
Assign individual contributors the different sections to be done Q3 2022
Collate, edit, finalize 1st paper December 2022
Start working on 2nd milestone 2nd Half 2021
Completed
Completed
Completed

## Slide 31: Working Group 3: Recap of Speaker Presentations
Date | Speaker | Entity | Topic
1/13 | Dr. Jithin Jagannath and Dr. Keyvan Ramezanpour | ANDROS Computational Solutions, LLC | Security Vulnerabilities in Coexistence of 5G and WiFI 6/6E
1/27 | Sundeep Rangan (Associate Director), Garg Siddharth, Elza Erkip, Christina Poepper | NYU Wireless | Introduction to NYU Wireless Center, Research direction pursing in 5G Security
2/10 | Dr. Ian Levy (NCSC Technical Director) | UK Cyber Security Center | UK for telecoms security
2/24 | Dr. Suku Nair (Ph.D, P.E., Director, SMU AT&T Center for Virtualization | SMU | 5G Security and Inter-Operability: Opportunities and Challenges
3/10 | Nagendra Bykampadi (Head of End-to-End Security Architecture, Assurance, and Ops); Co-chair O-RAN SFG | Rakuten Symphony | Security in a cloud native based Open vRAN
4/14 | John Morello | Palo Alto | NIST publication SP800-190 A container security guide. https://csrc.nist.gov/publications/detail/sp/800-190/final
4/28 | Scott Poretsky, MSEE, CISSP, Director of Security MANA Network Product Solutions | Ericsson | ZTA for Secure 5G Cloud Deployments
6/9 | Leo Popokh | HPE | 5G Slice Creation in compliance with 3GPP and ETSI

## Slide 32: Working Group 3: Next Steps
2 day in-person meeting July 20 & 21, 2022, Washington DC
Proposed Agenda:
  July 20
  All day working sessions to finalize paper framework & flow
  July 21
  2 hr. morning session with workgroup 2 - coordinate and collaborate on various areas
  Review of the past 2 days - Suzon Cameron and Billy Bob Brown to join

## Slide 33: Work Group 3 Expert Presentation Summaries

## Slide 34: Presentation 1: Security Vulnerabilities in Coexistence of 5G and WiFI 6/6E Presenter: Dr. Jithin Jagannath and Dr. Keyvan Ramezanpour from ANDROS Computational Solutions, LLC
Highlights:
Review of existing security vulnerabilities in the current 5G and Wi-Fi networks as a standalone network such as Layer 2 security.
Virtualized RAN and virtualized core:
  Most of the virtualization is currently happening on the core side.
  Virtualized core is most vulnerable due to their big data centers with highest risk of security compared to the virtualized RAN, given RAN represents the highest portion of the network and is expensive to be fully secure.
Virtualization and Access Network:
  If the virtualization technologies do not extend to the access network, it is to be contemplated as a potential risk exposing various gaps in-between.
  Similarly, access technologies that can reach the virtualized core exposes various security threats involved with virtualization.
Spectrum sharing with 5G, Wi-Fi, and attacker.
De-brief of various forms of authentications, Wifi Security Vulnerabilities (WPA3), and network architecture vulnerabilities.
Different types of attacks such as downgrade attack, side-channel attack, Dragonfly handshake protocol.
Counter measures: detection and provision.
5G coexistence new vulnerabilities within Wi-Fi, access network, and cellular core.
Wi-Fi off-loading:
  Instead of access through the towers, the access can also be via Wi-Fi. The hop from the Wi-Fi access vs the radio to the 5G core can expose potential vulnerabilities.
  Slicing extends to the radio network. Wi-Fi users from the non-3GPP devices if connect to the 5G core network is where the potential vulnerabilities can occur.

## Slide 35: Presentation 2: NYU Wireless Presenter: Sundeep Rangan (Associate Director), Garg Siddarth, Elza Erkip, Christina Poepper
Highlights:
Multivendor increases exposure
Untrusted segments of supply chain are Foundry and Digital hardware design, can lead to trojans in silicon and needs good focus, trusted segments being Network Equipment Provider and wireless carrier
Demonstrated user plane vulnerabilities for user data redirection & user impersonation due to missing integrity protection
Highlighted user data redirection, DNS request redirection and IP Header Checksum under the aLTEr attack
5G handover vulnerabilities for both intra and inter handover leading to either DoS or MitM relay
Recommended future work in:
  User plane Integrity Protection
  Enhanced Subscriber Privacy
  Interconnection Security
  Initial NAS Message Protection

## Slide 36: Presentation 3: UK for telecoms security Presenter: Ian Levy – technical director of national cybersecurity in NCSC (National Cyber Security Center) in UK
Highlights:
Brief history of 2017 cyberattacks in the UK telecom industry. The attack leading to 18 months long economic and technical modeling of telecommunications world with in-parallel understanding of how it actually works.
In total of 150 ways of attacks identified within telecom industry such as - espionage, using admin privileges, disrupt at small and large scale, national dependency, etc.
  TSR mentions in-depth management plane and signaling plane attacks.
  Brief discussion of TSR vs 5G tool-box.
Virtualization being adapted by the telecom industry for offering its robustness and resilience with added security benefits using modern signaling.
  Brief discussion on what does it mean to have virtualization vs containerization from the telecom and security aspect.
  VMs and containers mechanisms of virtualization and the difference between them with each technology’s pros and cons.
  Virtualization being a security function vs containerization is a scaling function.
  Containers are a mechanisms of virtualization. There are several other ways to virtualize than using containerization and VMs.
  With vibrant market of O-RAN virtualized industry, there are concerns with its alliance to security.
Strict policy compliance within security for telecommunications.
  Progression of technical specs into laws and having guidance.
  Vendor publishing statement of compliance as a strict regimen.
Hardware vs trusted software
  Dealing with hardware being easier than managing complex software from security perspective.
In order to gather more information regarding virtualized security, reach out to virtualization pioneers - VMware, Amazon, Google, Microsoft.
https://www.enisa.europa.eu/publications/5g-cybersecurity-standards/@@download/fullReport
https://www.enisa.europa.eu/publications/nfv-security-in-5g-challenges-and-best-practices/@@download/fullReport
Referenced documents in conversation

## Slide 37: Presentation 4: 5G Security and Inter-Operability: Opportunities and Challenges Presenter: Dr. Suku Nair (Ph.D, P.E., Director, SMU AT&T Center for Virtualizatio
Highlights:
5G security requires end-to-end security of all sections of the network, for example, RAN, Core, Internet, Control Plane, User Plane, Management Plane, etc.
Previously a mere authentication server used to suffice for the security, but with more complex systems such as 5G, server authentication is not enough. Therefore, introducing user authentication which also causing a lot more user attacks.
Issues with LTE/5G such as subscriber tracking, SS7 threats, no user plane integrity protection.
Various 5G security features based on CU/DU separation of gNB, subscriber privacy, unified authentication framework as well 5G for IOT, local network, authentication.
5G security comes with vertical (functional deployments) and horizontal (system including network, applications) levels.
Several outstanding challenges to manage the security for open-source platforms for cloud native, security automation, open source software, slice management, and IoT.
Example of a complex use case using a remote robotic surgery.
  Use of a fiber cable for its hepatic response in the beginning but extending the reach to wireless in the future with minimal latency, network delays between the surgeon and the robotic arm.
In conclusion:
3GPP does not standardize all aspects. Most of it is left to development and deployment.
Zero-trust architectures that defines each part of the network is independent making all aspects needs to be secure. This is a different approach to the older model of relying only on one trusted server.

## Slide 38: Presentation 5: Security in a cloud native based Open vRAN Presenter: Nagendra Bykampadi - Head of Security Architecture and Security Standards at Rakuten Symphony, and co-chair for the O-RAN Alliance Security Focus Group (SFG).
Highlights:
Overview comparison of RAN from a traditional layout to an open vRAN architecture.
Breakout of three types of open vRAN network topology into: aggregated DU vRAN, distributed DU vRAN, and distributed DU vRAN LLS-C1.
O-RAN's alliance to its architecture with its virtualized RAN network functions, hardware-software decoupling using cloud infra, and RIC.
  Note: Decoupling of software increases supply chain threats.
RAN specific landscape threats - additional functions (more code) reciprocates to additional attacks on the system.
Evolution roadmap of O-RAN security standards with 5G coinciding with each releases' safeguards' and up-coming planning.
Analysis of:
Threats and their protection measures of network interfaces in 5G system.
GSMA NESAS/SCAS 3GPP security assurance and test case specifications for virtualized gNB.
Security in Open vRAN.
Secure communications between the CNFs.
Interfaces description from 3GPP model as well newly introduced O-RAN protocols among which Non/Near-RT RIC and O2 interfaces being currently work in-progress.
Best security practices for CNF security:
Layered-block of several security in layers from infrastructure, Kubernetes, container, and application.
Kubernetes security: to have authenticated and authorized access into its control plane, securing data at the Rest level,
Containers security: across all stages and to avoid being noisy neighbors.
Disaggregation of key security differentiators between the traditional RAN and O-RAN.
Various ways the vDU and vCUs can expose threats to the front haul, mid-haul, and back-haul.

## Slide 39: Presentation 6: NIST Publication SP800-190. A container security guide. Presenter: John Morello from Palo Alto
Highlights:
SP800-190 covers: Threats and counter-measures through multiple layers of the stack, best practices around protecting the virtual machines and hosts applicable in the container world, fundamentals around vulnerability management and secure configuration.
Containers allow minimal host operating system reduces attack surface, evaluation of pre-deployment images, and look for vulnerabilities prior to production deployment.
Designed to be single-purpose focused entities that should maintain their same state throughout their lifecycle; the consistency allows security to be done in a more autonomous manner by creating a model by observing containers at the beginning of a life cycle.
Toolchain current state for containers can identify the artifacts contained within the container environment using images. Various tools are offered in the industry to do the software component analysis of these artifacts such as:
  Constant checks for vulnerabilities or security rule violations are performed in the build time while building the software.
  Check the distribution and deployment time for any mentioned vulnerabilities exist.
  Diversity and options in various tools offer how to store your code, conduct a build job, various ways of how to do deployment.
  Threshold for critical vulnerabilities check. In this case if there are vulnerabilities found beyond the set limit, the software is sent back to the vendor for control check.
For hybrid environment with virtual machines and container images:
  Virtual machines has less standardization around machine image formats.
  Disk image size for VM is found in GBs vs container images are in MBs.
  Large image sizes are not practical for easy transfer or image evaluation with build process.
  Containers provide the opportunity to potentially be more secure because of the efficiency that they provide making them secure and reliable.
  A hypervisor provides a greater degree of separation between individual entities that run above it than a container run-time does.
    A hypervisor allocate different tenants on a physical server using virtualization. Each of these tenant or virtualized OS may utilize containerization on top of this virtualized layer. In summary: a hypervisor is a hardware; a container run-time is an os layer.
  With most deployments being hybrid these days, the decision is to target the desired security dimension and then leverage the strengths of both layers in a customized order to get the solution with maximum advantage.
Greatest level of threat exists at the software application layer that is run on top and not as much on the underlying infrastructure running beneath.
  In the paper, it is recommended to group the applications by cluster levels of sensitivity, such as low, medium, and high criticality.
  Clusters are then separate from each other using hypervisor to avoid container escape or leakage using this isolation of hypervisor.
The best practices offered are generic and are applicable between all environments and networks.
  Some of the recommended check offs for infrastructure as a code, policies to not expose ssh to the outer world.
  More research to be done by the workgroup on finding various security templates.

## Slide 40: Presentation 7: ZTA for Secure 5G Cloud Deployments Presenter: Scott Poretsky, MSEE, CISSP, Director of Security MANA Network Product Solutions
Highlights:
Terminologies:
  Zero Trust - A concept that eliminates trust in digital systems based on the principal that no network user, packet, interface, or device should be trusted.
  Zero Trust Network Access (ZTNA) - Traditional perimeter security ensuring existence of authorization and authentication to gain remote access into a network or remote application. An IT security solution that provides secure remote access to an organization's applications, data, and services.
  Zero Trust Architecture (ZTA) - A plan (NIST 800-207) to be applied across any digital system. ZTA introduces the concept of perimeter less security and assumes that the adversary is already inside the network and moving laterally, according to CISA. ZTA includes ZTNA.
  Two definitions of ZTA for cloud deployments:
  NIST SP 800-207 - Introduces perimeter-less security. Based upon the principal that there is no implicit trust granted to an asset based upon ownership, physical location, or network location. This impacts the traditional way of securing the ORAN.
  CISA - An extension of ZTA and assumes that the adversary is already inside the network meaning we must protect the data as if the threat actor is already inside and can move laterally. (Protection is required for data in rest, data in motion as well data workloads to detect any suspicious movements.)
  USG Progression to ZTA in the 5G Cloud and various timelines:
  NIST SP 800-207 established in 2020 introduced 7 tenants.
  Solar-winds in 2020 lead to executive order in the White house EA 14028 calling on agencies to work on ZTA based on NIST establishment.
  CISA published its Cloud Security Technical Reference Architecture
  CISA Zero Trust Maturity Model containing 5 pillars
  OMB Zero Trust Cybersecurity Principles
  CISA Security Guidance for 5G cloud Infrastructure
  Log4j
  CISA Cloud Security Technical Reference Architecture highlights the connection between the cloud and ZTA.
  Being in cloud does not reciprocate to having a ZTA. Cloud services lets you enable the zero trust because the distributed nature of cloud necessitates additional configuration and management support in order to achieve the kind of security.
  CISA modernize its current cybersecurity programs, services, and capabilities to be fully functional with cloud-computing environments with ZTA.
  Telecommunication is one of the critical infrastructure categories for cloud security posture management oversees.
  ZTA can be very expansive and expensive making ZTA a long-term goal to strive towards while maintaining a risk-based analysis to your risk-based tolerance in a phased approach.
  In-parallel to protecting the inside of the cloud from internal thread actors, equal emphasis is needed to protect the resources themselves.
  CISA Security Guidance for 5G Cloud Infrastructures
  Primary highlights in regard to the 5G:
    Cloud-native 5G is a lucrative target for cyber threat actors
    In a hybrid or public cloud deployment, the MNO is accountable for the security posture of the deployment and apply a risk-based analysis.
    It is critical to continuously monitor for evidence of exploitation and adversarial lateral movement within 5G cloud deployments.
    This infrastructure offers four volumes of guidance and four security domains separately.
  3GPP 5G security are not zero trust architecture but several of the security points align with NIST 7 tenets of ZTA.
  ZTA in O-RAN is being applied to all work items and is covered as part of the NIST SP 800-207.

## Slide 41: Appendix

## Slide 42: Working Group 3: Methodology
Industry SME presentations
Standards bodies and industry associations (GSMA, CTIA, ETSI, 3GPP, NIST, ISO)
Individual contributor research gathered by Working Group members
Academic papers
Bi-weekly workgroup member meetings

## Slide 43: Discussion
WG3: Co-chairs
Micaela Giuhat, Microsoft
John Roese, Dell
WG3: Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks
Presenter – Jeff Goldthorp, FCC

## Slide 44: Presentation
WG4: Co-chairs
Mary Boyd, Intrado
Mark Reddish, APCO
WG4: 911 Service Over Wi-Fi

## Slide 45: Working Group 4: 911 Service Over Wi-Fi
June 15, 2022
Co-chairs:
Mary Boyd, Intrado Life & Safety
Mark Reddish, APCO
FCC Liaison: Rasoul Safavian

## Slide 46: Working Group 4: Background
The Chairwoman of the FCC directs CSRIC VIII to explore the public safety benefits, technical feasibility, and cost of options for making Wi-Fi access points and/or unlicensed spectrum available to the public to facilitate access to 911 services. The ubiquitous nature of Wi-Fi access points suggests that, in the long term, various Wi-Fi solutions could be added to the “toolbox” of 911 connectivity options available to consumers, Public Safety Answering Points (PSAPs), and communications providers, and could complement the broader transition to an IP-based Next Generation 911 environment.

## Slide 47: Working Group 4: Objectives
Bring industry stakeholders together to examine a range of technical issues with the goal of promoting consensus in the Wi-Fi ecosystem to support reliable 911 services (voice and text) under normal conditions and when catastrophic events disrupt mobile service. The primary focus will be to:
examine and report on security issues including authentication and access control protocols, solutions to automatically activate Wi-Fi Calling on eligible mobile devices, when necessary;
automatically determining the 911 caller location and call routing issues, 911 call prioritization, identifying missing standards, and timelines and costs for implementing 911 over Wi-Fi solutions.

## Slide 48
Working Group 4: Members
  *Also a CSRIC VIII Member
Brandon Abley,* National Emergency Number Association
Rob Alderfer,* Charter Communications
Mark Annas,* City of Riverside Fire Department, OEM
Michael Bergman,* Consumer Technology Association
Wade Buckner,* International Association of Fire Chiefs
Kirk Burroughs, Apple
Chinmay Dhodapkar, Google LLC
Stephen Edge, Qualcomm Technologies, Inc.
Katherine Elkins,* NHTSA
Harold Feld,* Public Knowledge
Fred Frantz, ANDRO Computational Solutions
Mark Gibson, CommScope
James D. Goerke, Texas 9-1-1 Alliance
Jeanna M. Green, T-Mobile
Kevin Green, Somos, Inc.
Mark Grubb, CISA
Mark Hess,* Comcast Corporation
Craig Hodan,* National Weather Service/NOAA
Everett Kaneshige,* NATOA
Robert Kubik, Samsung Electronics America
William 'Andy' Leneweaver, Washington State Military Department
Jason Lish,* Lumen Technologies, Inc.
Susan Miller,* ATIS
Charles (“Peter”) Musgrove, AT&T, Inc.
Theresa Reese, Ericsson
Travis Reutter,* ACA Connects- America's Communications Association
Charlie Sasser, National Association of State Technology Directors
Tim Schram,* NARUC
Sean Scott,* SecuLore Solutions
Malcolm Smith, Cisco Systems, Inc.
Stuart Strickland, Hewlett Packard Enterprise
Jeff Torres, Verizon Communications
Steve Watkins,* Cox Communications
Jeffrey Wittek, Motorola Solutions
William Mikucki, Comtech Telecommunications
Co-chairs: Mary Boyd,* Intrado
Mark Reddish,* APCO
FCC Liaison: Rasoul Safavian

## Slide 49
Working Group 4: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Chris Anderson, Lumen Technologies, Inc.
  Carol Ansley, Cox Communications
  Scott Blue, Cisco
  Tom Breen, SecuLore Solutions
  Matthew Chappell, Cox Communications
  Nicholas Garcia, Public Knowledge
  J. David Grossman, CTA
  Brian Hurley, ACA Connects
  Christian Militeau, ATIS
  Darrin Morkunas, Intrado
  James B. Ramsay, NARUC
  Praveen Srivastava, Charter Communications
  Peter Thornycroft, Hewlett Packard Enterprise
  Alison Venable, APCO
  Megan Stapleton, Comtech Telecommunications

## Slide 50: Working Group 4: Deliverables/Schedule
Sub-Teams established:
  Technical Feasibility (Active)
  Public Safety Benefits (Active)
  Cost (Awaiting outcomes of Technology & Benefits)
Meeting Schedules:
  Bi-Weekly (Full WG)
  Weekly / Bi-Weekly (Sub-Teams)
Baseline Report – In draft
Final Report on 911 Service over Wi-Fi, March 2023

## Slide 51: Sub-Team WG4: Technical Feasibility
Activities
  Draft framework for report contributions (Completed)
  Framework for use case analysis (Completed)
  Analysis of current network architectures / emergency Wi-Fi call flow (In Progress)
  Use Case development and analysis (many contributions in progress)
  Recommendations (TBD)
Status
  Active
  Weekly Meetings

## Slide 52: Sub-Team WG4: Public Safety Benefits
Activities
  Draft framework for report contributions (Completed)
  Use Case development and analysis (many contributions in progress)
  Recommendations (TBD)
Recommendations (TBD)
Status (Active)

## Slide 53: Working Group 4: Next Steps
Weekly & Bi-Weekly Meetings: Continue
Draft: Baseline Report (In Progress)

## Slide 54: Discussion
WG4: Co-chairs
Mary Boyd, Intrado
Mark Reddish, APCO
WG4: 911 Service Over Wi-Fi

## Slide 55: Presentation
WG5: Managing Software & Cloud Services Supply Chain Security for Comm. Infrastructure
WG5: Interim Co-Chairs
Todd Gibson, T-Mobile
Padma Sudarsan, VMware

## Slide 56: Working Group 5: Managing Software & Cloud Services Supply Chain Security for Communications Infrastructure
June 15, 2022
Interim Co-Chairs: Todd Gibson, T-Mobile & Padma Sudarsan, VMware
FCC Liaison: Saswat Misra

## Slide 57: Working Group 5: Background
The Chairwoman of the FCC directs CSRIC VIII to review risks to service provider operations from attacks in service providers’ software and cloud services stacks and develop mitigation strategies for these vulnerabilities. In order to improve supply chain security in the communications industry, the FCC has barred the use of Universal Service Fund support to pay for equipment and services produced or provided by any company posing a national security threat to the integrity of communications networks or the communications supply chain, and the FCC will be reimbursing providers to remove, replace, and dispose of insecure equipment and services. Additionally, prior CSRIC work, such as the CSRIC IV Report on Cybersecurity Risk Management and Best Practices (March 2015), and the CSRIC II Report on Cybersecurity Best Practices (March 2011), focused on attacks that mostly affect traffic on the network or attacks on users through the network.
However, recent breaches of trusted vendors of software have exposed risks in other segments of the supply chain that have resulted in previously trusted systems becoming compromised. Specifically, attackers have inserted malware in to signed code with valid, but compromised, digital certificates. These recent breaches have highlighted that the threat is pervasive and extends well beyond the telecommunications network itself to software components and cloud-based services that service providers rely on to manage and operate their networks. Attacks on these operational networks could have a significant impact on emergency 911 calls and national security communications.
The FCC further directs CSRIC VIII to recommend best practices to mitigate the risks for each vulnerability it identifies, considering the matrix of capabilities of large and small service providers, large and small software vendors, and large and small cloud service providers.

## Slide 58
Working Group 5: Members
  *Also a CSRIC VIII Member
Rob Alderfer,* Charter Communications
Tom Anderson, ATIS
Jan H.L. (John-Luc) Bakker, BlackBerry Corporation
Donna Bethea-Murphy,* Inmarsat
Shirley Bloomfield,* NTCA-The Rural Broadband Association
Matt Carothers, Cox Communications
Josh Cech, S&T Telephone Cooperative Association
Dana Golub,* Public Broadcasting Service
Anu Jagannath, ANDRO Computational Solutions
Mohammad Khaled, Ericsson
Jason Lish,* Lumen Technologies, Inc.
Timothy May, * NTIA
Martin McGrath, Nokia
Maureen C. Mclaughlin,* Satellite Industry Association
George Popovich, Motorola Solutions
Travis Reutter,* ACA Connects- America's Communications Association
Nasrin Rezai,* Verizon Communications
John Roznovsky, Mavenir
Sean Scott,* SecuLore Solutions
Jim Stringer, AT&T, Inc.
Richard “Dick” Tenney, CISA
Claire Vishik,* Intel
Kelly Williams, NAB
Timothy Wilson-Johnston, Cisco Systems, Inc.
Henry Young,* BSA | The Software Alliance
Timothy Youngblood,* T-Mobile
Interim Co-Chairs: Todd Gibson, T-Mobile & Padma Sudarsan, VMWare
FCC Liaison: Saswat Misra

## Slide 59
Working Group 5: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Reza Arefi, Intel
  Tom Breen, SecuLore Solutions
  Mark Carmel, CISA
  Cathleen M. Dwyer, Verizon Communications
  Brandon Hinton, Satellite Industry Association
  Brian Hurley, ACA Connects
  Tamber Ray, NTCA - The Rural Broadband Association
  Jason VonBargen, Charter Communications
  Mark Roy, Public Broadcasting Service
  John A. Schiel, Lumen Technologies, Inc.

## Slide 60: Working Group 5: Milestones/Schedule
Milestones:
Best Practices to Improve Communications Supply Chain Security, September 2022
  Primary focus is on the Software Supply Chain for the first report.
  Goal is to generate novel Recommendations in matrix form for the identified gaps from other published papers and/or reports.
Best Practices to Improve Supply Chain Security of Infrastructure and Network Management Systems, June 2023
  No activities has been started for this report yet.
  Focus will be on Hardware Supply Chain and Implicit Trust of NMS Software Supply Chain
Meeting Schedule:
  Currently once every two weeks
  Plan to change to weekly meetings until Sept 2022 report is complete

## Slide 61: Working Group 5: Progress
New Microsoft Teams workspace has been created to enable WG collaboration.
Contributions/Updates to date in the forming Sept 2022 Report:
  Todd Gibson – authored the Executive Summary, Introduction, and Recommendation Matrix format/subsections.
  Dick Tenney – authored the Objective, Scope, Methodology, Commerce/DHS Assessment on Supply Chain, Log4j, and Kaseya VSA subsections.
  Tamber Ray, Shirley Bloomfield, and Josh Cech – authored inputs from the Small Service Provider perspective including Analysis/Recommendations.
  Josh Cech – authored the Synopsys 2022 Open-Source Security and Risk Analysis Report subsection.
  John-Luc Bakker – authored analysis on the EO 14028 and Secretary of Commerce Minimum Elements for a SBOM
  John Schiel – authored analysis on NSTAC’s Report to the President – Software Assurance in the Information and Communications Technology and Services Supply Chain.
  John Roznovsky – authored analysis relating to Countries of Concern
  Tom Anderson – authored subsections with analysis of ATIS Supply Chain Standard Whitepaper and SolarWinds
  Jim Stringer – authored subsections with analysis on NIST’s Software Supply Chain Security and Publish Guidance of Practices that Enhance Software Supply Chain Security reports.

## Slide 62: Working Group 5: Next Steps
Sept 2022 Report: continue with the priority focus on the Analysis, Findings, Recommendation, and Conclusion Sections.
June 2023 Report: engage WG on the creation of two sub-workgroups to start on the research and analysis needed for the June 2023 report:
  Recommended Best Practices to Improve Supply Chain Security of:
    Infrastructure
    Network Management Systems

## Slide 63: Discussion
WG5: Managing Software & Cloud Services Supply Chain Security for Comm. Infrastructure
WG5: Interim Co-Chairs
Todd Gibson, T-Mobile
Padma Sudarsan, VMware

## Slide 64: Presentation
WG6: Co-chairs
Farrokh Khatibi, Qualcomm Francisco Sanchez, SBA
WG6: Leveraging Mobile Device Applications and Firmware to Enhance WEA

## Slide 65: Working Group 6: Leveraging Mobile Device Applications and Firmware to Enhance Wireless Emergency Alerts
Co-chairs:
  Farrokh Khatibi, Qualcomm Technologies, Inc.
  Francisco Sanchez, U.S. Small Business Administration (SBA)
FCC Liaison: James Wiley
June 15, 2022

## Slide 66: Working Group 6: Background
The Chairwoman of the FCC directs CSRIC VIII to identify the software or functional requirements necessary to allow Wireless Emergency Alerts (WEA) software to pull capabilities from other mobile device applications and firmware to enhance the presentation of WEA alert messages. When WEA launched, mobile device manufacturers in collaboration with Commercial Mobile Service Providers that participate in WEA created specific programming procedures and rules for allowing their WEA applications to access and retrieve WEA messages. These programming procedures and rules are not available to third-party developers and do not currently allow the WEA software to interface with other mobile device functionality. This policy protects consumer privacy and the integrity of WEA messages, but also prevents WEA from leveraging many mobile device capabilities that could make WEA’s presentation of emergency information to the public more effective. To provide just two examples, researchers have found that allowing WEA to leverage the mapping capabilities of popular smartphone applications could reduce the amount of time the public spends trying to confirm that an emergency alert is relevant to them before taking action to protect their lives and property. Mobile devices also often contain a suite of accessibility features that, if leveraged in the WEA context, could make the emergency information that WEA messages contain more accessible to individuals with access and functional needs.

## Slide 67: Working Group 6: Objectives
To define an Application Programming Interface (API) to enable mobile device capabilities that could make WEA’s presentation of emergency information to the public more effective, including any features necessary to continue to secure WEA messages and protect consumer privacy. In addition to technical issues, CSRIC VIII should also identify any resource constraints or procedural issues that could affect the timely deployment of this Application Programming Interface and recommend appropriate mitigations.

## Slide 68: Working Group 6: Deliverables/Schedule
Report on WEA Application Programming Interface, March 2023

## Slide 69: Working Group 6: Members
FCC Liaison: James Wiley
  *Also a CSRIC Member
Co-chairs: Farrokh Khatibi,* Qualcomm
Francisco Sanchez,* U.S. Small Business Administration (SBA)
Mark Annas,* City of Riverside Fire Department, OEM
Rebecca Baudendistel, NYC Emergency Management
Terri Brooks, T-Mobile
Wade Buckner,* International Association of Fire Chiefs
Kirk Burroughs, Apple
Brian K. Daly,* AT&T, Inc.
Harold Feld,* Public Knowledge
Craig Fugate,* America’s Public Television Stations
Michael Gerber, National Weather Service/NOAA
Dana Golub,* Public Broadcasting Service
Stephen Guiwits, US Geological Survey
Mark Hess,* Comcast Corporation
Antwane Johnson,* FEMA
Robert Kubik, Samsung Electronics America
Jennifer Lazo, City of Los Angeles Emergency Management Dept.
John Marinho, CTIA
Susan Miller,* ATIS
Krisztina Pusok,* American Consumer Institute
Matthew Straeb, Global Security Systems, LLC
Peter Tomczak,* FirstNet Authority
Dara Ung, Comtech Telecommunications Corp.
Larry Walke, National Association for Broadcasters
Steve Watkins,* Cox Communications
Chia-Kaung (Jack) Yu, Google LLC

## Slide 70: Working Group 6: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Tim Dunn, T-Mobile
  Nicholas Garcia, Public Knowledge
  Kevin Green, FirstNet Authority
  Al Kenyon, FEMA
  Edward Longe, American Consumer Institute
  Charles (“Peter”) Musgrove, ATIS
  Peter Scott, PBS

## Slide 71: Working Group 6: Status
Working Group Membership: Finalized
Working Group Meetings
  Bi-weekly conference calls, with additional calls as needed
Document Library Established (ATIS Workspace)
  Contributions / Reference Documents / Calendars

## Slide 72: Working Group 6: Status
Reviewed existing WEA parameters available in the handset.
Reviewed Application Programming Interface (API) in the handset for Android and iOS Operating Systems.
Compiling a list of relevant use cases and analyzing them to determine which ones:
  could be supported by exposing existing WEA parameters to secure applications;
  may require enhancements to the existing WEA (i.e., new parameters required);
  may require major changes to the existing WEA, require alternative alerting techniques, or they are beyond the scope of WEA;
  may require standards, policy, and/or legislative changes.
Some use cases are outside the scope of CSRIC VIII WG6, but will be included in the report for future consideration.
Updating the draft report.

## Slide 73: Working Group 6: Next Steps
Conduct routine bi-weekly conference calls
  Continue to analyze use cases
  Develop new Recommendations
  Update the draft report
Provide periodic status updates to Steering Committee and Council

## Slide 74: Discussion
WG6: Co-chairs
Farrokh Khatibi, Qualcomm Francisco Sanchez, SBA
WG6: Leveraging Mobile Device Applications and Firmware to Enhance WEA

## Slide 75: Closing Remarks
CSRIC VIII Co-chair
Billy Bob Brown, CISA

## Slide 76: Adjourn Meeting Suzon Cameron, DFO

## Slide 77: NEXT CSRIC VIII MEETING SEPTEMBER 21, 2022 at 1:00 pm EDT